## Slide 1: NVMe Over Fabrics
The objectives of this project are to assemble and benchmark a functional protocol stack. The stack will provide high throughput transfers with low CPU utilization that could be ported to Hewlett Packard Enterprise’s 3Par storage systems. To benchmark the servers, we created a custom test suite that determined read, write, buffer size, and seek performance.
[Put in a statement about results regardless of whether they are positive or negative]
Abstract
    Network block device over Accelio framework
    Presented as a regular storage block device on the local system
    Fast IO to remote devices through its use of accelio acceleration facilities and multi-queue implementation in the block layer
    Library for high-performance asynchronous IO using RDMA
    Provides Zero-copy data delivery
    Designed for multi-core CPUs and multi-threaded applications
    Remote Direct Memory Access (RDMA) is capable of allowing server to server data movement management with minimal CPU involvement
    Provides a lossless connection on top of the Ethernet protocol by implementing the Data center bridging enhancements (DCB) to the Ethernet standard.
    Bridges, converges, and controls the flow of multiple classes of traffic over an Ethernet network
    Hardware support for RDMA
    Interconnect system for the I/O ports that supports 40G Ethernet
Functional Protocol Stack
Results
Testing Methodology
Test suite:
FIO and the ib_send_* family of commands run by Python benchmarking framework
Data results were automatically parsed and output to CSV files, allowing for easy graph creation.
FIO was used to test nbdX and local ramdisk sequential and random read/write speeds, collected in the form of IOPS, bandwidth, and transfer latency.
A ramdisk was used on the server to emulate a fast storage device because we did not have access to a suitable NVMe SSD.
Data gathered:
Bandwidth/Latency of RoCE connection
Bandwidth/Latency/IOPS of nbdX device and local ramdisk
John Gemignani, Coy Humphrey, Eric Litvinsky, Jayden Navarro, Alice Yu, Kevin Cheng*
nbdX
Accelio
RoCE v2 (RDMA over Converged Ethernet)
Converged Ethernet
HP Infiniband FDR Ethernet Card/Infiniband QSFP+ Interface
We would like to thank:
Samuel Fineberg, Ph.D., Distinguished Technologist, Storage Chief Technologist Office at Hewlett Packard Enterprise
Dr. Linda Werner, Ph.D., Faculty Advisor, UCSC
Daniel Fava, Graduate Teaching Assistant, UCSC
Hewlett Packard Enterprise for the hardware and support provided
* Participated in the first half of the project
Acknowledgments
Conclusion
Through our benchmarking, we have found that the current nbdX technology was able to perform [well | poorly] compared to a local ramdisk in terms of IOPS, throughput, and latency. In terms of overall use, we found nbdX to suffer from many of the pitfalls that are commonly seen in emerging technologies, such as stability issues and a lack of edge case handling. A new driver is due to be released in the coming months by the NVMe over Fabrics Consortium, and is foreseen to replace the current nbdX software. The new driver is expected to improve the reliability of the technology. With increased stability with the new driver, Accelio supported networks should benefit from lower CPU utilization, faster data transfers, and lower latency compared to their non-RDMA equivalent infrastructures.
Chart: IOPS
| 4K Block Size | 32K Block Size
1 IO Depth | 4646 | 3494
32 IO Depth | 143513 | 59555
64 IO Depth | 134475 | 75250
Chart: Bandwidth
| 4K Block Size | 32K Block Size
1 IO Depth | 18586 | 111820
32 IO Depth | 574055 | 1905771
64 IO Depth | 537903 | 2408021
Chart: Latency
| 4K Block Size | 32K Block Size
1 IO Depth | 212 | 282
32 IO Depth | 222 | 536
64 IO Depth | 475 | 850
We felt that the current technology showed promise in terms of its ideal benchmarking results. We were impressed by the achieved IOPS, bandwidth, and latency, and how they compared to other enterprise solutions. With the advent of faster NVMe attached SSD, Accelio based data-center network technologies should be able to support transfers at near local PCIe throughput and latency, eliminating the current network bottleneck.
Analysis
Graph 1: [We have the IOPS for block sizes and IO depths. We’ll compare them against the same metrics for enterprise NVMe drives. And if ours is greater, then we can eliminate nbdX as a bottleneck for these drives.
Graph 2: [We have the bandwidth for block sizes and IO depths. We’ll compare them against the same metrics for enterprise NVMe drives. And if ours is greater, then we can eliminate nbdX as a bottleneck for these drives.]
Graph 3: [We’ll compare the latency again the latency for current solutions.]