## Slide 1: NVMe Over Fabrics
The objectives of this project are to assemble and benchmark a functional RDMA based network protocol stack for implementing NVMe over Fabrics. NVMe over Fabrics is a standardized solution for efficient access to fabric attached non-volatile memory [1]. The stack provides high throughput transfers with low CPU utilization to be ported to Hewlett Packard Enterprise’s 3Par storage systems. To benchmark the servers, we created a custom test suite that determined read and write performance. From the results, we conclude this will eliminate the network stack as a bottleneck in accessing remote NVMe storage.
Abstract
Functional Protocol Stack
Results
Testing Methodology
Test suite:
FIO and the ib_send_* family of commands run by Python benchmarking framework
Data results were automatically parsed and output to CSV files, allowing for easy graph creation.
FIO was used to test nbdX and local ramdisk sequential and random read/write speeds, collected in the form of IOPS, bandwidth, and transfer latency.
A ramdisk was used on the server to emulate a fast storage device because we did not have access to a suitable NVMe SSD.
Data gathered:
Bandwidth/Latency of RoCE connection
Bandwidth/Latency/IOPS of nbdX device and local ramdisk
John Gemignani, Coy Humphrey, Eric Litvinsky, Jayden Navarro, Alice Yu, Kevin Cheng⃰
nbdX
Accelio
RoCE v2 (RDMA over Converged Ethernet)
Converged Ethernet
HP FDR Ethernet Card/Infiniband QSFP+ Interface
We would like to thank:
Samuel Fineberg, Ph.D., Distinguished Technologist, Storage Chief Technologist Office at Hewlett Packard Enterprise
Dr. Linda Werner, Ph.D., Faculty Advisor, UCSC
Daniel Fava, Graduate Teaching Assistant, UCSC
Hewlett Packard Enterprise for the hardware and support provided ⃰ Participated in the first half of the project
Acknowledgments
Conclusion
Through our benchmarking, we have found that the current nbdX technology was able to perform well compared to a local ramdisk in terms of IOPS, throughput, and latency. In terms of overall use, we found nbdX to suffer from many of the pitfalls that are commonly seen in emerging technologies, such as stability issues and a lack of edge case handling. A new driver is due to be released in the coming months by the NVMe over Fabrics Consortium, and is foreseen to replace the current nbdX software. The new driver is expected to improve the reliability of the technology. With increased stability from the new driver; Accelio supported networks should benefit from lower CPU utilization, faster data transfers, and lower latency compared to their non-RDMA equivalent infrastructures.
We believe that the current technology shows promise in terms of its ideal benchmarking results. We were impressed by the achieved IOPS, bandwidth, and consistently low CPU utilization (< 25%). With the advent of faster NVMe attached SSD; Accelio based data-center network technologies should be able to support transfers at near local PCIe throughput and latency, eliminating the current network bottleneck.
Analysis
Graph 1: nbdX was able to yield > 250,000 4K IOPS on 32, 64, and 128 IO depths. Compared to the ~100,000 4K IOPS of NVMe attached drives, the network stack will not be the IOPS bottleneck for remote transfers.
Graph 2: On large block sizes, nbdX performed close to our maximum link speed (37 Gb/s). Compared to the ~8.0 Gb/s transfer speeds of NVMe attached drives, the network stack will not be the throughput bottleneck for remote transfers.
Graph 3: For the tested block sizes and IO depths, nbdX performed within the expected latency range of remote transfer protocols.
    Network block device over Accelio framework
    Presented as a regular storage block device on the local system
    Pre-specification version of NVMe over Fabrics
    Library for high-performance asynchronous IO using RDMA
    Provides Zero-copy data delivery
    Designed for multi-core CPUs and multi-threaded applications
    Remote Direct Memory Access (RDMA) is capable of allowing server to server data movement management with minimal CPU involvement
    Provides a lossless connection on top of the Ethernet protocol by implementing the Data center bridging enhancements (DCB) to the Ethernet standard.
    Bridges, converges, and controls the flow of multiple classes of traffic over an Ethernet network
    Hardware support for RDMA
    Interconnect system for the I/O ports that supports 40Gb Ethernet
[1] SNIA Ethernet Storage Forum http://www.snia.org/sites/default/files/ESF/NVMe_ Under_Hood_12_15_Final2.pdf
References
Chart: IOPS
| 4K Block Size | 32K Block Size | 64K Block Size | 128K Block Size
1 IO Depth | 10240 | 9962 | 9726 | 8221
32 IO Depth | 268537 | 94786 | 62302 | 34687
64 IO Depth | 297702 | 128480 | 64880 | 35200
128 IO Depth | 264118 | 129275 | 69481 | 35209
Chart: Bandwidth
| 4K Block Size | 32K Block Size | 64K Block Size | 128K Block Size
1 IO Depth | 0.32769 | 2.5504 | 4.9802 | 8.419
32 IO Depth | 8.5932 | 24.2654 | 31.8988 | 35.5201
64 IO Depth | 9.5265 | 32.8911 | 33.219 | 36.0449
128 IO Depth | 8.4518 | 33.0946 | 35.5747 | 36.0542
Link Speed | 37 | 37 | 37 | 37
Chart: Latency
| 4K Block Size | 32K Block Size | 64K Block Size | 128K Block Size
1 IO Depth | 387.7235 | 398.7216 | 408.2483 | 483.1561
32 IO Depth | 476.12 | 1349.813 | 2053.7392 | 3687.8857
64 IO Depth | 859.3332 | 1991.5096 | 3943.3627 | 7269.1727
128 IO Depth | 1937.5684 | 3958.706 | 7364.4767 | 14528.4147